|  | ......................... pcs. .............................. € .............................. € GEZE Slimdrive SL RC 2 Modular, compact automatic linear sliding door with only 70 mm drive height, RC 2 tested in accordance with DIN V ENV 1627 to 1630, TÜV type-tested in accordance with DIN 18650, for leaf weights up to 120 kg per leaf Integrated battery for emergency opening and closing in the event of a power failure Intelligent digital control (Category 2 in accordance with DIN EN 954-1 and Performance Level “d” in accordance with DIN EN ISO 13849-1): - Self-learning - Optimum convenience thanks to automatic adaptation of door behaviour to traffic - Can be networked and integrated in building systems via CAN-bus - Independent fault detection and protocol - Adjustment options for all door movement parameters - All functions integrated in one unit, no further modules necessary Extremely quiet running direct current drive Robust power supply with integrated all-pole main switch and fuse Static and dynamic power limitation in compliance with DIN 18650, as well as static under 150 N in accordance with ASR A1.7 (formerly BGR 232) Automatic reversal when obstacles are detected Drive dimensions (H x D): 70 x 189 mm - Reinforced roller carriage version - Additional mechanical protection in the upper horizontal area Floor guide: - Pointwise floor guide, made of anodised aluminium E6/EV1, can be installed on finished floor - Reinforced supporting bracket near the floor guide as anti-leverage protection for the moving leaves ( ) Mounting sub-structure for supporting angle for stable fixing on unfinished floor Locking: - Bi-stable electromechanical rod locking, invisibly integrated in the profile system, with manual emergency unlocking in the drive ( ) Mounting sub-structure for floor plate for the rod locking mechanism for stable fixing on unfinished floor Type of installation: ( ) Wall installation or ( ) Installation on profile system Construction dimensions (dimensions in unfinished state): Clear overall height LH:............... mm Clear construction width LW:............... mm Passage height PH:.............. mm (max. 3000 mm) Passage clearance PC:............. mm (double-leaf 900 - 3000 mm) Application range: No. of leaves ( ) double-leaf ( ) with side parts Fitting: ( ) moving leaf with ISO or mono-safety glass fine-framed (up to 120 kg leaf weight): ( ) with ISO (safety glass P4A) <23.5 mm sealed on the internal and external moving leaf edge ( ) with VSG (safety glass P4A) <23.5 mm sealed on the internal and external moving leaf edge Surface of the light alloy parts of the drive and the moving leaves if appropriate: ( ) anodised EV1 or ( ) RAL ........ Wiring to be carried out on site according to the GEZE cable diagram by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650 through plant fitters or service partner. In compliance with DIN 18650: - Safety analysis must be carried out as a basis for planning and execution - An inspection must be carried out at least 1 x year and after-sales service maintenance at least 1 x year Note The burglar-resistant function RC2 is only enabled in "NIGHT" mode. In "NIGHT" mode the door does not fulfil any escape route requirements. It is necessary to ensure that there is nobody in the building or that sufficient other emergency exits are available. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Operation GEZE display programme switch in the AS 500 range for setting the mode of operation as well as for commissioning and parameterisation of the drive, with function keys, 2x 7-segment display, alphanumerical fault display, IP rating IP 40 Operating modes: permanently open, automatic, shop closing, night-locking, off ( ) Surface-mounted ( ) Flush-mounted or GEZE key programme switch for setting the operating mode, with control keys, LED dot display, coded error display, IP rating IP 40, suitable for switch product ranges with 55 x 55 mm switch insert Operating modes: off, permanently open, automatic, shop closing-time, night-locking ( ) Surface-mounted ( ) Flush-mounted or GEZE mechanical programme switch for setting the operating mode, with rotary button, LED fault display, IP rating IP 40, suitable for switch programmes with 55 x 55 mm switch insert Operating modes: off, permanently open, automatic, shop closing-time, night-locking ( ) Surface-mounted ( ) Flush-mounted or GEZE mechanical programme switch for setting the operating mode, with key, LED fault display, IP rating IP 40, suitable for switch programmes with 55 x 55 mm switch insert Operating modes: off, permanently open, automatic, shop closing-time, night-locking ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Operation (optional position) GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the operating mode, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Activation and protection (optional position) GC 363+ combined detector with direction detecting radar movement detector for activation and active infrared detector with two light curtains for protection of the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) outside ( ) inside Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the sensor in the ceiling ( ) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Activation and protection (optional position) GC 365 combined detector with direction detecting radar movement detector for activation and active infrared detector with two light curtains for protection of the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) outside ( ) inside Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the sensor in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 339+ active infrared detector with two light curtains for protecting the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling ( ) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 341 active infrared detector with two light curtains for protecting the opening or closing area according to DIN 18650/EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE elbow switch, plastic, IP rating IP 30 Dimensions: 90 x 180 x 23 mm ( ) white ( ) stainless steel ( ) optional transmitting module ( ) Surface-mounted ( ) Rear panel for attaching the elbow switch to glass (in connection with the transmitting module) or GEZE elbow switch, LS990, IP rating IP 30 Dimensions: 81 x 223 x 51 mm ( ) white ( ) stainless steel ( ) optional transmitting module ( ) Surface-mounted ( ) Flush-mounted or GEZE elbow switch, stainless steel, IP rating IP 65 Dimensions: 72 x 250 x 17 mm ( ) Surface-mounted or GEZE non-contact proximity switch (radar) Plastic with antimicrobial surface, IP rating IP65, multi-colour LED feedback, adjustable acoustic feedback. Additional input to actively change the LED colour. Dimensions: 80 x 80 mm ( ) Flush mounting 12 mm deep ( ) Surface mounting 21 mm deep ( ) Variant for WC or GEZE LED sensor push button, plastic, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor push button, glass, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor foot switch, glass, IP rating IP69K Dimensions: 100 x 100 x 3 mm ( ) flush-mounting ( ) vertically adjustable installation base for depths of up to 215 mm from the unfinished floor |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE wireless programme with secure rolling code encryption for wireless activation of the drive (approx. 30 m range in the building). Transmitter: ( ) Wireless transmitter with 1 key, IP rating IP 54 and wall fixing ( ) Wireless transmitter with 2 keys, IP rating IP 54 and wall fixing ( ) Wireless transmitter with 4 keys, IP rating IP 54 and wall fixing ( ) Transmitting module for optional integration in GEZE elbow switches Receiver: ( ) Receiving module with 2 outputs, 24 V, pulse mode or pulse and permanent mode for installation in the drive or in a flush-mounted box with IP rating IP 20 |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE GCER 300, 1-door SET Access control solution with RFID reader and PIN keypad in stand-alone operation for controlling one door (can be extended to 2 doors). RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Two authorisation types for short-time release or continuous release (office function). Configurable door release time. Variable PIN length. Communication between reader and control unit takes place by encrypted data transfer. Functions such as interlocking door system or dementia adjustable. Release buttons can be connected. Set comprising: 1 pc. GEZE GCER 300 I/O Box (ID no. 185707) 1 pc. GEZE GCVR 300 T, RFID reader flush-mounted (ID no. 185708) 2 pc. GEZE GCER 300 system card master (ID no. 185713) 10 pc. GEZE RFID ID card (ID no. 185711) Optional GEZE GCVR Touch 300 T, RFID reader flush-mounted (ID no. 187108) GEZE RFID key fob (ID no. 185712) GEZE GCER AP surface-mounted frame (Id. no. 130024) or GEZE GCER 300 Light, 1-door SET Access control solution with RFID reader and PIN keyboard in stand-alone operation with a relay output for controlling one door located in the secured inner area. RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised for short-time release. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Configurable door release time. Variable PIN length. Communication takes place via encrypted data transfer. Set comprising: 1 pc. GEZE GCER 300 Light, RFID reader flush-mounted (ID no. 185710) 1 pc. GEZE GCER 300 system card master (ID no. 185713) 10 pc. GEZE RFID ID card (ID no. 185711) Optional GEZE RFID key fob (ID no. 185712) GEZE GCER AP surface-mounted frame (ID no. 130024) Accessories for GCER 300 / GCER 300 Light Plug-in power supply NT 1.0 A – 24 V DC (optional) Primary: 230 V AC, 50 Hz Secondary: 24 V DC (+/- 5 %) / 1 A (ID no. 130025) Power supply NT 1.1 A – 24 V DC flush-mounted (optional) For installation in deep standard flush-mounted boxes Primary: 230 V AC, 50 Hz Secondary: 24 V DC / 1.1 A (ID no. 151426) Power supply NT 1.5 A – 24 V DC HA (optional) For installation on top hat rails Primary: 230 V AC, 50 Hz Secondary: 21.6 – 26.4 V DC / 1.5 A (ID no. 151425) |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch outside (IP rating IP 54) with or without profile half cylinder and switch function ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch outside (IP rating IP 54) with or without profile half cylinder and hold-open function for the fire service ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch outside (IP rating IP 54), prepared for on site profile half cylinder of closing system and 1 push button switch with key symbol for opening from the inside. On contact, the system opens from its locked position once outwards and inwards, and locks again after the leaf has reached the closed position. |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE additional pushbutton for limited opening width |
|  | ......................... pcs. .............................. € .............................. € Safeguarding GEZE safety leaf for protecting against shearing and nipping spots in accordance with DIN 18650 with post-rail structures (depending on the offset between post surface and facade glassing) behind the moving leaf, leaf made of 10 mm ESG incl. fitting alternatively: ( ) sensor-controlled side panel protection using 3D light curtain |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE safety photoelectric barrier with 2 transmitters and 2 radio receivers for protecting the opening width, IP rating IP 65 (according to DIN 18650 only permissible if a radar movement detector is used on both sides, door leaf power is limited by a power limitation system and not for people in need of special protection) |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE emergency stop switch with glass pane and lighting for switching off the mains voltage, IP rating IP 20 An emergency command device (emergency stop switch) is not essential in accordance with DIN 18650. ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE emergency stop switch with illuminated mushroom button for emergency opening or emergency unlocking, IP rating IP 40 An emergency command device (emergency stop switch) is not essential in accordance with DIN 18650. ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |