|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer system TS 4000 IS, for double leaf doors, for installation on fire and smoke protection doors, with infinitely adjustable closing force size 1 – 6 in accordance with EN 1154, with integrated closing sequence control; closing force, closing speed and back check are front adjustable, with visual closing force display, standard installation on door leaf/hinge side, with mounting plate Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) acc. to RAL |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |
|  | ......................... pcs. .............................. € .............................. € GEZE RSZ 7 smoke switch control unit, suitable for installation on fire and smoke protection closers, extendable, with telescopic function, for bridging unfavourable lintel situations, 30 mm overall height, in GEZE design, with adaption of the alarm threshold, contamination indicator and integrated test button, integrated line monitoring to ceiling-mounted detector and manual trigger switch, for connection of GEZE hold-open devices, approved by DIBt as hold-open system for fire protection closers, EN 14637 compliant Connection: 230V AC Output voltage: 24 V DC, 250 mA For lintel height > 1 m, 2 additional ceiling-mounted detectors are needed. Colour: ( ) silver-coloured ( ) white ( ) stainless steel effect ( ) RAL ….. |
|  | ......................... pcs. .............................. € .............................. € GEZE hold-open magnets, Operating voltage 24 V DC, Power consumption 1.5 W Retention force 490 N ( ) Hold-open magnet basic model (zinc plated without base plate) for in-wall installation or installation in any construction ( ) Hold-open magnet for wall mounting with base plate ( ) Hold-open magnet for flush-mounted installation ( ) Hold-open magnet for surface installation ( ) Base for hold-open magnet surface-mounted for floor installation ( ) Hold-open magnet with spacer tube zinc plated for floor/ceiling/wall mounting with swivelling magnetic head ( ) Version in basic length 185 mm ( ) Version in basic length 335 mm ( ) Hold-open magnet wall mounting, basic length 65 mm GEZE Magnetic counter plates, ( ) Standard magnetic counter plate on mounting plate with spring system for flatness with hold-open magnet ( ) Magnetic counter plate with spring buffer on installation housing with damping spring for soft spring buffer for heavy doors ( ) Magnetic counter plate, swivelling on mounting plate with swivelling magnetic counter plate for angle positions between door and hold-open magnet |
|  | ......................... pcs. .............................. € .............................. € GEZE manual trigger switch (compulsory for hold-open magnets and freeswing function) ( ) Surface-mounted ( ) Flush-mounted |